## Slide 1: Supply Side and Demand Side
Practical Course: Smart Energy Systems Sandro Speth, Markus Zilch, Dominik Wagner

## Slide 2: Weather Service

## Slide 3: Weather Service
  Weatherbit.io
    Free online weather service
    API Key needed
    Two APIs for gathering weather data
      Current weather: https://api.weatherbit.io/v2.0/current
        Query String parameter: key, lat, lon, units (optional)
      24 hours weather forecast on hourly basis: https://api.weatherbit.io/v2.0/forecast/hourly
        Query String parameter: key, lat, lon, units (optional)
    1000 requests per day

## Slide 4: Weather Service
  Weatherbit.io

## Slide 5: WeatherCollector
  Data used
    lat: Latitute
    lon: Longitute
    timestamp_utc: UTC Timestamp
    rh: Relative humidity in %
    pres: Air pressure in mb
    wind_spd: wind speed in m/s
    temp: Temperature in Celsius
    ghi: Global horizontal solar irradiance in W/m^2

## Slide 6: WeatherCollector
  Two HTTP REST endpoints
    Create new WeatherCollector object by location
      Path: POST /weathercollectors
      Body as application/json: { "lat" : <lat>, "lon" : <lon> }
      Response as application/json: { "lat": <lat>, "lon": <lon>, "id": <id> }
      Response status code: 201, 400
    Delete WeatherCollector object of given location
      Path: DELETE /weathercollectors
      Body as application/json: { "id": <id> }
      Response status codes: 200, 400

## Slide 7: Energy generation

## Slide 8: Windturbine

## Slide 9: Windturbine
  Energy produced:
  0.5 * areaSwept * moistAirDensity * windSpeed^3 * efficiencyCoefficient
  Area swept:
  r^2 * PI
  Windspeed and efficiencyCoefficient :
  User Input

## Slide 10: Windturbine
  Moist air density:
  Compound of dry air and water vapor and their respective densities
  Depends on:
      Temperature
      Pressure
      Relative humidity
  Formula:
      d = density
      p = pressure
      R = specific gas constant

## Slide 11: Windturbine
    Partial pressure of dry air and water vapor:
    Total pressure -> Partial pressure of dry air + partial pressure of water vapor
    Partial vapor pressure computable with the formula:
      Relative humidity * saturated vapor pressure
    Partial dry air pressure:
      Measured air pressure – partial vapor pressure
    Saturated vapor pressure:
      => Herman Wobus equation, only depends on the Temperature and a lot of constants

## Slide 12: Photovoltaic

## Slide 13: Photovoltaic
    Energy generated:
    module area * solar panel yield * performance ratio * solar radiation incident
    User inputs:
    Module area and Watt peak
    Depends on:
    Temperature
    Solar radiation
    Day of the year

## Slide 14: Photovoltaic
    Solar panel yield is the percentage of:
    Watt peak in kW / module area in m^2
    Performance ratio:
    All other losses combined + temperature loss
    Temperature loss:

## Slide 15: Photovoltaic
    Solar radiation incident:
    Solar panels are mostly tilted
    Solar radiation is tilted based on the day of the year and the latitude of the measurement
    The solar radiation incident describes the effective solar radiation in a tilted surface based on:
      horizontal sun power in W/
      Elevation angle alpha
      Solar panel tilt beta

## Slide 16: Photovoltaic
    Elevation angle alpha:
    90 – latitude of panel + delta
    Declination angle delta:
    23.45 * sin(360/365 * (284 * day of the year))
    To get the solar radiation incident the following equation can be used:
    Horizontal sunpower * (sin(alpha*beta)/sin(alpha))

## Slide 17: Battery

## Slide 18: Battery
    For the battery we set the interval for charging and discharging to one hour.
    The equation given in the slides therefore becomes easier.
    The equation in the implementation uses max and min functionalities to ensure the constraints of the battery as defined in the slides hold true.

## Slide 19: Demand side

## Slide 20: Demand side
    For the demand model we implemented 2 different profiles:
      normal consumers
      commercial consumers
    For both we calculated the power demand per m² based on the hour of the day.
    To get the power demand of a specified consumer type one therefore only must specify the area, the occupation (between 1 and 0) and the hour of the day:
      Consumption[h] * area * occupation

## Slide 21: Home
Chart: Demand Profile for DE_KN_residential2_grid_import
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 0.16609 | 0.13141 | 0.11719 | 0.11464 | 0.11773 | 0.12757 | 0.14173 | 0.21606 | 0.26719 | 0.27981 | 0.30423 | 0.29299 | 0.32416 | 0.33442 | 0.27879 | 0.26336 | 0.27528 | 0.26491 | 0.32066 | 0.37708 | 0.39127 | 0.37046 | 0.2987 | 0.23783
 | 0.16609 | 0.13141 | 0.11719 | 0.11464 | 0.11773 | 0.12757 | 0.14173 | 0.21606 | 0.26719 | 0.27981 | 0.30423 | 0.29299 | 0.32416 | 0.33442 | 0.27879 | 0.26336 | 0.27528 | 0.26491 | 0.32066 | 0.37708 | 0.39127 | 0.37046 | 0.2987 | 0.23783
 | 0.16609 | 0.13141 | 0.11719 | 0.11464 | 0.11773 | 0.12757 | 0.14173 | 0.21606 | 0.26719 | 0.27981 | 0.30423 | 0.29299 | 0.32416 | 0.33442 | 0.27879 | 0.26336 | 0.27528 | 0.26491 | 0.32066 | 0.37708 | 0.39127 | 0.37046 | 0.2987 | 0.23783
 | 0.16609 | 0.13141 | 0.11719 | 0.11464 | 0.11773 | 0.12757 | 0.14173 | 0.21606 | 0.26719 | 0.27981 | 0.30423 | 0.29299 | 0.32416 | 0.33442 | 0.27879 | 0.26336 | 0.27528 | 0.26491 | 0.32066 | 0.37708 | 0.39127 | 0.37046 | 0.2987 | 0.23783

## Slide 22: Office building
Chart: Demand Profile for DE_KN_industrial3_grid_import
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 67.8182 | 65.2201 | 63.5356 | 62.6774 | 61.1737 | 60.5207 | 59.958 | 59.698 | 61.1268 | 72.25 | 85.8932 | 129.3718 | 104.5949 | 116.581 | 114.3883 | 103.7301 | 106.218 | 100.7878 | 93.1374 | 86.769 | 82.8793 | 78.2221 | 72.2463 | 68.5716

## Slide 23: Demo